## Slide 1
Honeywell
Technical Architecture Version | Phase 2
Connected Care and Hospital Operations Platform
A technically rich architecture view using existing WSP product, prototype, and component visuals
Patient telemetry
Edge + APIs
Command center
2026 India and APAC Innovation Challenge
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
1

## Slide 2
Honeywell
Technical thesis
Architecture demonstration
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
2
Honeywell extends the wearable smart patch into a hospital-grade connected-care architecture spanning sensing, edge, interoperability, workflow intelligence, and command-center operations.
Device ecosystem
Patch, BP, SpO2, bed sensors, asset tags.
Resilient edge
Authentication, buffering, protocol normalization, gateway orchestration.
Platform services
Registry, assignment, time-series ingest, rules, alerts, analytics.
Hospital apps
Nurse, doctor, bed board, asset map, leadership command center.
Technical objective: one event-driven hospital operating layer

## Slide 3
Honeywell
Existing visual baseline
Images reused from WSP source decks
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
3
Industrial design render
Reusable patch housing, LED indication, button, USB-C opening.
Prototype kit
Physical WSP unit, ECG cable, charger, and lead interface.
Electrode-side concept
Electrode placement concept for ECG and body-contact sensing.
Source visuals embedded from existing concept and MVO documents

## Slide 4
Honeywell
Wearable patch hardware architecture
Current MVO component baseline
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
4
ESP32-S3-MINI-1 MCU + Wi-Fi + BLE
MAX30003 ECG AFE
TMP1075 Skin temp
ADXL367 Posture + motion
MAX20356 PMIC Charger + power path + fuel gauge
450 mAh Li-Po Rechargeable battery
USB-C + ECG lead cable Power + data + sensor interface
RGB LED + button Status + wakeup
Debug UART Manufacturing + support
Hardware role
Patient-worn telemetry endpoint for ECG, temperature, posture, movement, derived respiration, device health, and future vitals expansion.

## Slide 5
Honeywell
Patch signal pipeline
From body signal to actionable telemetry
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
5
Body contact ECG/temp/motion
Analog front end filter + sample
MCU processing packetize + status
Wi-Fi/BLE telemetry authenticated send
Edge ingest buffer + normalize
Rules + dashboard alerts + trends
Sampling and packet cadence configurable by clinical workflow and battery budget.
Telemetry contains sensor values, timestamp, device ID, battery, RSSI/connectivity state, and firmware/config version.
Edge buffering protects against temporary hospital Wi-Fi disruption.
Platform association links every payload to patient, bed, ward, and care episode.

## Slide 6
Honeywell
Expanded device ecosystem
Clinical and operational telemetry endpoints
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
6
Wearable patch
Continuous ECG, HR, temperature, respiration, posture, restlessness.
Connected BP + SpO2
Telemetry role
Periodic vitals capture during ward rounds and high-risk monitoring.
Bed state input
Telemetry role
Occupied, vacant, cleaning, blocked, transfer, discharge-ready, maintenance.
Asset tags
Telemetry role
BLE, Wi-Fi, RFID, or UWB tags for pumps, monitors, cylinders, carts, wheelchairs.
Unified event model across clinical signals and operations events

## Slide 7
Honeywell
Connectivity and edge topology
Hospital-grade connectivity under network variability
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
7
Patch + BP + SpO2
Wi-Fi / BLE
Bed sensors
BLE / wired input
Asset tags
BLE / RFID / UWB
Mobile workflows
Tablet / workstation
Honeywell Edge Gateway Auth + buffer + normalize + route
Device registry
Time-series ingestion
Event bus + rules
Command center APIs
Edge resilience
Local buffering, retry logic, time synchronization, device-health monitoring, and controlled reconnect behavior support hospital network variability.

## Slide 8
Honeywell
Event-driven data architecture
Telemetry, workflow state, and analytics separation
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
8
Raw telemetry store
Sensor payloads, ECG snapshots, vitals values, device metadata, timestamps.
Operational event stream
Bed state changes, asset zone events, assignment changes, alert lifecycle.
Rules outputs
Thresholds, trends, missed-vitals windows, battery/connectivity, bed/asset exceptions.
Workflow tasks
Nurse queue, doctor review, housekeeping queue, biomedical action, transport task.
Analytics aggregates
Ward, hospital, and hospital-chain KPIs for throughput, acuity, utilization, response.

## Slide 9
Honeywell
Patient-bed-device assignment model
Avoiding orphan telemetry
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
9
Patient
Data keys
MRN / episode / demographics
Admission
Data keys
ward / department / care episode
Bed
Data keys
bed ID / state / location
Device
Data keys
serial / firmware / battery / status
Asset
Data keys
tag ID / class / zone / service state
Assignment service responsibilities
Pair device to patient, patient to bed, asset to zone, and events to care episode with auditability.
Why it matters
Every telemetry point, bed event, and asset event is traceable to the right operational context.

## Slide 10
Honeywell
Rules engine and alerting
Clinical and operations logic in one configurable layer
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
10
Vitals threshold
BP, HR, SpO2, temperature, ECG-derived alerts
Trend detection
Change over baseline, repeated abnormalities, escalation windows
Missed vitals
Expected observation not received within defined time
Device health
Battery, RSSI, offline, firmware/config mismatch
Bed workflow
Cleaning delay, blocked bed, discharge-ready queue
Asset exception
Missing asset, zone exit, service due, low utilization
Alert lifecycle: generated -> routed -> acknowledged -> resolved -> audited

## Slide 11
Honeywell
Bed management technical model
State machine plus workflow queues
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
11
Vacant
Occupied
Discharge-ready
Cleaning
Blocked
Maintenance
Transfer
State inputs
ADT feed
Nurse/ward update
Housekeeping update
Maintenance status
Transfer request
Workflow queues
Admission queue
Cleaning queue
Transport queue
Maintenance queue
Discharge coordination
Operational KPIs
Turnaround time
Blocked-bed time
Cleaning cycle time
Occupancy
Transfer bottlenecks
Bed intelligence connects patient acuity, capacity, and hospital flow

## Slide 12
Honeywell
Asset tracking architecture
Accuracy tiers matched to operational value
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
12
BLE tags
Low cost zone proximity for pumps, wheelchairs, monitors.
RFID gates
Entry/exit control for storerooms, wards, departments.
UWB zones
Higher precision for critical assets and high-value equipment.
Wi-Fi tags
Network-based location where infrastructure supports it.
Asset event model
tag_id, asset_class, zone, timestamp, movement event, utilization state, service state, exception type, assigned department

## Slide 13
Honeywell
Hospital integration architecture
API-first, adapter-ready interoperability
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
13
Hospital systems HMS / EHR / EMR
Integration adapter FHIR / HL7 / REST
Platform services ADT + assignment + alerts
Applications Dashboards + APIs
Inbound hospital context
ADT, patient demographics, ward, bed, encounter, clinician assignment.
Outbound platform events
Alerts, vitals summaries, device events, bed-state updates, asset exceptions.
Mapping controls
Hospital-specific data dictionaries, interface monitoring, retry/error handling.
Integration pattern supports heterogeneous India and APAC hospital environments

## Slide 14
Honeywell
Security and compliance architecture
Controls across device, edge, platform, and users
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
14
Device identity
Provisioning, device registry, serial binding, firmware/config visibility.
Secure transport
Authenticated ingestion, encryption in transit, controlled gateways.
Access control
Role-based access for nurse, doctor, biomedical, operations, admin, leadership.
Auditability
Assignment changes, alert lifecycle, integration events, device actions.
Network segmentation
Device, edge, platform, and hospital integration zones separated.
Deployment control
On-premise, private cloud, or hybrid data-retention policies.

## Slide 15
Honeywell
Deployment topology
Ward, hospital, and hospital-chain scale
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
15
Ward deployment 50-100 beds
Hospital deployment Multiple wards + ops
Chain deployment Multi-site dashboards
Enterprise Analytics
Ward package
Patch devices, BP/SpO2, BLE gateway, nurse dashboard, basic alerts.
Hospital package
Bed board, asset tags, integration adapter, command-center workflows.
Enterprise package
Multi-site KPIs, analytics aggregates, standard deployment template.

## Slide 16
Honeywell
Technical non-functional requirements
Architecture guardrails for hospital operations
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
16
Reliability
Buffered edge telemetry, retry logic, device health monitoring.
Scalability
Ward-to-chain architecture with event partitioning and modular services.
Maintainability
Device registry, firmware/config visibility, interface monitoring.
Interoperability
FHIR/HL7 where available, REST adapters for local hospital systems.
Usability
Role-specific dashboards and exception-first workflows.
Traceability
Telemetry-to-patient-to-bed-to-event lineage and audit logs.

## Slide 17
Honeywell
End-to-end technical demo flow
How the platform demonstrates value
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
17
1. Assign
Patient + bed + patch + BP device
2. Capture
ECG, vitals, posture, temperature, device health
3. Normalize
Edge authentication, buffering, payload normalization
4. Evaluate
Rules for trends, thresholds, missed vitals, battery, connectivity
5. Act
Nurse queue, doctor review, bed board, asset map, command center
6. Analyze
Ward KPIs, throughput, utilization, enterprise reporting
Demo story: sensor signal becomes operational action and measurable KPI

## Slide 18
Honeywell
Technical differentiators
Architecture-led healthcare platform
Impact by Honeywell
Technical Architecture Version | India and APAC Innovation Challenge - Phase 2
18
Honeywell sensing foundation connected to hospital workflow intelligence.
Multi-domain architecture for vitals, bed state, asset tracking, and command-center operations.
Edge resilience for real-world hospital network variability.
Integration-aware design for heterogeneous India and APAC hospital systems.
Scalable event model supporting ward deployment, hospital operations, and chain-level analytics.
From wearable telemetry to whole-hospital technical architecture